## Slide 1
RASPBERRY PI PICO 2W
Getting Started with MQTT
MicroPython · Publish / Subscribe · HiveMQ · BME280 / DHT22 Sensor
Lecture Duration: 3–6 Hours Level: Intermediate | MicroPython Required
MQTT Stack
Publisher (Pico 2W)
MQTT Broker (HiveMQ)
Subscriber (Pico / App)
Reference: randomnerdtutorials.com/raspberry-pi-pico-w-mqtt-micropython/
Instructor: Sros Nhek, Ph.D.

## Slide 2
Lecture Contents
3–6 Hour Roadmap
01
Introduction to MQTT
What it is, why it matters for IoT
02
MQTT Core Concepts
Pub/Sub, Topics, Messages, Broker
03
MQTT Broker Setup
HiveMQ Cloud, Mosquitto options
04
Installing umqtt Modules
simple.py, robust.py via Thonny
05
Configuration File
secrets, boot.py, Wi-Fi connection
06
Publishing Messages
Sensor data → broker → topic
07
Subscribing to Topics
Receive commands, control outputs
08
Testing & Troubleshooting
MQTT Explorer, debug tips

## Slide 3
Prerequisites & Parts Required
What you need before starting
Raspberry Pi Pico 2W
Wi-Fi-enabled board with MicroPython flashed
Thonny IDE / VS Code
Installed and board recognized over USB
BME280 / DHt22 Sensor
Temperature, Humidity & Pressure (I²C)
Wi-Fi Network
2.4 GHz router with internet access
HiveMQ Account
Free cloud MQTT broker (no install needed)
BME280 Wiring
Pin | Pico 2W
VCC | 3.3V
GND | GND
SDA | GP4
SCL | GP5
DHt22 Wiring
Pin | Pico 2W
VCC | 3.3V
GND | GND
Data | GP15

## Slide 4
SECTION 01
Introduction to MQTT
What it is · Why IoT needs it · RFC 6455 · History

## Slide 5
What is MQTT?
Message Queuing Telemetry Transport
Definition
MQTT stands for Message Queuing Telemetry Transport.
It is a lightweight publish-subscribe messaging protocol designed for constrained devices and low-bandwidth, high-latency networks.
Standard:
OASIS Standard & ISO/IEC 20922
Port:
1883 (plain) / 8883 (TLS)
Transport:
TCP/IP
Versions:
3.1.1 (most common) · 5.0
Use Cases:
IoT, Home Automation, Telemetry
Why MQTT for IoT?
Lightweight:
Minimal header overhead (2 bytes min). Perfect for microcontrollers with limited RAM.
Low Bandwidth:
Designed for slow, unreliable networks. Works over 2G/3G, LoRa, Wi-Fi.
Async Delivery:
Broker stores messages for offline devices (with retained messages).
Many-to-Many:
One publisher → broker → many subscribers simultaneously.
Secure:
TLS/SSL encryption + username/password authentication.
Notes: TLS (Transport Layer Security) and SSL (Secure Sockets Layer) are cryptographic protocols designed to secure communications over a computer network. They protect sensitive data—like passwords and payment details—from being intercepted by eavesdroppers while in transit between a client (like your web browser) and a server. [1]

## Slide 6
HTTP vs MQTT Comparison
Choosing the right protocol for your project
Feature | HTTP | MQTT
Communication | Request–Response (pull) | Publish–Subscribe (push/pull)
Connection | New connection per request | Persistent long-lived connection
Overhead | ~800 B HTTP headers/request | 2–4 byte MQTT frame header
Server push | Not possible (polling needed) | Native server-to-client push
Multi-client | Each client polls separately | Broker fans out to all subscribers
Best for | REST APIs, file downloads | Sensor data, IoT control, dashboards
URL scheme | http:// / https:// | mqtt:// / mqtts://
State | Stateless | Stateful (session, subscriptions)

## Slide 7
SECTION 02
MQTT Core Concepts
Publish / Subscribe · Topics · Messages · Broker · QoS

## Slide 8
Publish / Subscribe Model
The heart of MQTT communication
PUBLISHER
Pico 2W
(BME280 data)
publishes on topic:
pico/temperature
BROKER
HiveMQ / Mosquitto
Filters & routes
messages by topic
Stores retained msgs
Manages sessions
Phone
App
Node-RED
Dashboard
Another
Pico 2W
SUBSCRIBERS
All subscribed to:
pico/temperature

## Slide 9
MQTT Topics
Hierarchical addressing with forward slashes
Topic Structure
Topics are UTF-8 strings separated by forward slashes ( / ). Each level narrows the scope:
home/office/lamp
home/bedroom/temperature
pico/sensor/humidity
pico/led/control
factory/line1/motor/rpm
⚠ Topics are CASE-SENSITIVE: Pico/Temp ≠ pico/temp
Wildcards
+ (single level)
Matches exactly one level
home/+/lamp → matches
home/office/lamp
home/bedroom/lamp
# (multi level)
Matches any remaining levels
home/# → matches
home/office/lamp
home/bedroom/temp
home/kitchen/fan

## Slide 10
MQTT Messages & Quality of Service
QoS levels and message payload
Message Payload
MQTT messages can carry any payload — plain text, JSON, binary, or sensor values. The broker delivers them without interpreting content.
# Payload examples
client.publish("pico/temp", "24.5")
client.publish("pico/data", '{"t":24.5,"h":60}')
client.publish("pico/led", "ON")
Retained Messages
When retain=True, the broker stores the LAST message on that topic. New subscribers instantly receive it without waiting for the next publish.
client.publish(topic, msg, retain = True)
Quality of Service (QoS)
QoS 0 — At most once
Fire-and-forget. No acknowledgement. May be lost. Lowest overhead.
QoS 1 — At least once
Message acknowledged by receiver. May be delivered more than once.
QoS 2 — Exactly once
4-way handshake. Guaranteed delivery, no duplicates. Highest overhead.

## Slide 11
The MQTT Broker
The message routing engine
The broker is the central hub of MQTT. It receives ALL messages, filters by topic, and delivers to all interested subscribers.
HiveMQ Cloud
Cloud-hosted, free plan available. No install needed. Best for beginners and production IoT.
✓ Free tier ✓ TLS built-in ✓ Web UI ✓ No setup
✗ Requires internet access
Mosquitto (Local)
Open-source broker on Raspberry Pi or PC. Most popular in hobbyist and home automation projects.
✓ Free & open-source ✓ Local network
✓ No internet needed ✓ Lightweight
✗ Requires install & configuration
Mosquitto (Cloud VPS)
Mosquitto installed on a cloud server
(e.g., DigitalOcean). Accessible worldwide from anywhere.
✓ Internet accessible ✓ Full control
✓ Low cost VPS
✗ Requires Linux admin skills
In this lecture: HiveMQ Cloud (free). The code is compatible with any MQTT broker — just update the connection details.

## Slide 12
SECTION 03
Setting Up HiveMQ Broker
Cloud MQTT · Account Setup · Cluster URL · Access Credentials

## Slide 13
HiveMQ Cloud Setup
Step-by-step broker configuration
1
Create Account
Go to hivemq.com → click 'Start Free' → choose HiveMQ Cloud plan → register or login.
2
Get Cluster URL
After login, click 'Manage Cluster'. Copy the Cluster URL (e.g. abc123.s1.eu.hivemq.cloud). Save it — you'll need it in your code.
3
Create Credentials
Click 'Access Management' tab → fill in Username and Password → set permission to Publish and Subscribe → click 'Create Credential'.
4
Collect Details
Before proceeding, make sure you have: ① Cluster URL ② MQTT Username ③ MQTT Password ④ Port: 8883 (TLS)
Port 8883 (TLS/SSL) is required for HiveMQ Cloud. Plain port 1883 will not connect. Set ssl=True in your MicroPython MQTT client.

## Slide 14
MQTT Broker Details Checklist
Information needed before writing code
Required Details
MQTT Server / URL:
abc123.s1.eu.hivemq.cloud
Port (TLS):
8883
Username:
your_hivemq_username
Password:
your_hivemq_password
Client ID:
pico2w_01 (unique per device)
Security Tips
Store credentials in secrets.py — never hardcode in main.py
Add secrets.py to .gitignore before pushing to GitHub
Use TLS (port 8883) — plain text port 1883 exposes credentials
Use unique Client IDs — duplicate IDs cause disconnection loops
Rotate passwords periodically in production deployments
Using Mosquitto instead?
Just change the server URL to your Raspberry Pi's local IP (e.g. 192.168.1.10), port to 1883, and set ssl=False. The rest of the code stays identical.

## Slide 15
SECTION 04
Installing umqtt Modules
simple.py · robust.py · Thonny IDE file upload · Directory structure

## Slide 16
umqtt Library Overview
MicroPython MQTT client modules
umqtt.simple
simple.py
Core MQTT client. Supports connect, publish, subscribe, wait_msg. Lightweight but does NOT auto-reconnect.
Key Methods:
MQTTClient(id, server)
connect()
publish(topic, msg)
subscribe(topic)
set_callback(fn)
wait_msg()
umqtt.robust
robust.py
Extends simple.py with automatic reconnection. Best for long-running IoT deployments where Wi-Fi or broker drops occasionally.
Key Methods:
Inherits all simple.py methods
reconnect() — auto-reconnects
wait_msg() — with reconnect on error
Suitable for production use
Both modules must be placed in a folder called umqtt/ on the Pico filesystem. Source: github.com/micropython/micropython-lib

## Slide 17
Installing umqtt via Thonny IDE
Step-by-step file upload to Pico filesystem
1
Open Files Sidebar
In Thonny IDE → View → Files. You'll see two panels: your computer (top) and Pico 2W filesystem (bottom).
2
Create umqtt Directory
Right-click on the Pico 2W panel → New Directory → type umqtt → click OK. The folder appears in the sidebar.
3
Create simple.py
Right-click on the umqtt folder → New File → name it simple.py. Paste the code from the GitHub link (see below).
4
Create robust.py
Repeat step 3 for robust.py. Paste the robust.py code. Both files must be inside the umqtt/ folder.
5
Verify Structure
In Thonny's Pico panel you should see: /umqtt/simple.py and /umqtt/robust.py. You're ready to import!
Pico 2W Filesystem
/
├── boot.py
├── main.py
├── secrets.py
└── umqtt/
├── simple.py
└── robust.py
Download links: github.com/RuiSantosdotme/Random-Nerd-Tutorials → Projects/Raspberry-Pi-Pico/MicroPython/mqtt/umqtt/

## Slide 18
SECTION 05
Configuration & Boot Files
secrets.py · boot.py · Wi-Fi Connection · MQTT Credentials

## Slide 19
Creating secrets.py
Keeping credentials out of your main code
# secrets.py — NEVER share this file publicly!
# Add secrets.py to .gitignore before using Git
# Wi-Fi credentials
WIFI_SSID = "Your_WiFi_Name"
WIFI_PASSWORD = "Your_WiFi_Password"
# MQTT broker details (HiveMQ example)
MQTT_SERVER = "abc123.s1.eu.hivemq.cloud"
MQTT_PORT = 8883
MQTT_USER = "your_hivemq_username"
MQTT_PASSWORD = "your_hivemq_password"
MQTT_CLIENT_ID = "pico2w_01"
Security Best Practices
Never hardcode credentials directly in main.py or publish.py
Create a .gitignore file with: secrets.py
Import from secrets: from secrets import WIFI_SSID, MQTT_SERVER, ...
Importing in your scripts
# In boot.py / main.py:
from secrets import (
WIFI_SSID, WIFI_PASSWORD,
MQTT_SERVER, MQTT_PORT,
MQTT_USER, MQTT_PASSWORD,
MQTT_CLIENT_ID
)
Then use WIFI_SSID, MQTT_SERVER, etc. as normal variables throughout your code.
Mosquitto users:
Set MQTT_PORT = 1883 and ssl = False in the connect call. If no password is required, pass user = None and password = None.

## Slide 20
boot.py — Wi-Fi Connection
Auto-run on power-up; connects Pico 2W to Wi-Fi
# boot.py — runs automatically on every boot
import network, time
from secrets import WIFI_SSID, WIFI_PASSWORD
def connect_wifi():
wlan = network.WLAN(network.STA_IF)
wlan.active(True)
if not wlan.isconnected():
print("Connecting to Wi-Fi...")
wlan.connect(WIFI_SSID, WIFI_PASSWORD)
timeout = 0
while not wlan.isconnected() and timeout < 20:
time.sleep(1) ; timeout += 1
print(".", end="")
if wlan.isconnected():
print("\nConnected!")
print("IP:", wlan.ifconfig()[0])
else:
print("Wi-Fi FAILED")
return wlan
connect_wifi() # Called on boot automatically
boot.py Behavior
Auto-runs first
boot.py runs before main.py on every power-up or reset.
Network ready
By the time main.py runs, Wi-Fi is already connected.
Reusable
Import connect_wifi() from boot if needed in main.
Timeout guard
20-second loop prevents infinite hang on bad credentials.
Status codes
STAT_GOT_IP = 3 = success. -2 = no AP. -3 = wrong password.

## Slide 21
MQTT Client Connection Helper
Connecting to the broker in MicroPython
from umqtt.simple import MQTTClient
from secrets import MQTT_SERVER, MQTT_PORT, MQTT_USER, MQTT_PASSWORD, MQTT_CLIENT_ID
def connect_mqtt():
client = MQTTClient(
client_id = MQTT_CLIENT_ID,
server = MQTT_SERVER,
port = MQTT_PORT,
user = MQTT_USER,
password = MQTT_PASSWORD,
keepalive = 60,
ssl = True, # Required for HiveMQ (TLS port 8883)
ssl_params = {"server_hostname": MQTT_SERVER}
)
client.connect()
print("Connected to MQTT broker")
return client
MQTTClient Parameters
param | description
client_id | Unique ID for this device
keepalive | Ping interval in seconds (0=disabled)
ssl=True | Enable TLS — required for port 8883
Mosquitto (local)?
Set port=1883, ssl=False, remove ssl_params. If anonymous access, set user=None and password=None. Everything else stays the same.

## Slide 22
SECTION 06
Publishing MQTT Messages
Sensor Data · BME280 · Topics · JSON Payloads · Retained

## Slide 23
Reading BME280 Sensor
Temperature · Humidity · Pressure over I²C
# Install BME280 library first:
# Thonny → Tools → Manage Packages → 'bme280'
from machine import Pin, I2C
import bme280, time
# I2C setup: SDA=GP4, SCL=GP5
i2c = I2C(0, sda=Pin(4), scl=Pin(5), freq=400000)
bme = bme280.BME280(i2c=i2c)
# Read sensor values
values = bme.values
# values returns: ('24.50C', '60.23%', '1013.25hPa')
# Or read raw floats:
temp = round(bme.temperature, 2)
hum = round(bme.humidity, 2)
pres = round(bme.pressure, 2)
print(f'Temp: {temp}°C Hum: {hum}% Pres: {pres} hPa')
BME280 Quick Facts
Parameter | Value
Interface | I²C or SPI
Address | 0x76 or 0x77
Temp range | -40 to +85 °C
Hum accuracy | ±3% RH
Pressure | 300–1100 hPa
Pico Pins | GP4 (SDA), GP5 (SCL)
Install BME280 library: Thonny → Tools → Manage Packages → search 'bme280' → install 'micropython-bme280'.

## Slide 24
Complete Publish Script — publish.py
Sending BME280 sensor data to MQTT broker
# publish.py — publish BME280 sensor data every 10 seconds
import time, json
from machine import Pin, I2C
import bme280
from umqtt.simple import MQTTClient
from secrets import MQTT_SERVER, MQTT_PORT, MQTT_USER, MQTT_PASSWORD, MQTT_CLIENT_ID
# Topics
TOPIC_TEMP = "pico/bme280/temperature"
TOPIC_HUM = "pico/bme280/humidity"
TOPIC_PRESS = "pico/bme280/pressure"
# Hardware
i2c = I2C(0, sda=Pin(4), scl=Pin(5), freq=400000)
bme = bme280.BME280(i2c=i2c)
# Connect to broker
client = MQTTClient(MQTT_CLIENT_ID, MQTT_SERVER, MQTT_PORT,
MQTT_USER, MQTT_PASSWORD, ssl=True, ssl_params={"server_hostname": MQTT_SERVER})
client.connect()
print("MQTT connected!")
while True:
temp = str(round(bme.temperature, 2))
hum = str(round(bme.humidity, 2))
pres = str(round(bme.pressure, 2))
client.publish(TOPIC_TEMP, temp, retain=True)
client.publish(TOPIC_HUM, hum, retain=True)
client.publish(TOPIC_PRESS, pres, retain=True)
print(f'Published: {temp}°C | {hum}% | {pres} hPa')
time.sleep(10) # Publish every 10 seconds

## Slide 25
Publish Code — Deep Dive
Understanding each part of publish.py
Topic Design
pico/bme280/temperature
Follow a hierarchy: device/sensor/measurement. Consistent naming makes dashboards and filtering much easier to manage.
MQTTClient()
client = MQTTClient(id, server, port, user, pwd, ...)
Creates the client object. Does NOT connect yet — just configures parameters. Call .connect() separately.
client.connect()
Initiates TCP + MQTT handshake with the broker
Sends CONNECT packet. Broker replies with CONNACK. If credentials are wrong, raises MQTTException.
client.publish()
publish(topic, msg, retain=True)
Sends PUBLISH packet. retain=True stores last value on broker — new subscribers get it immediately without waiting for next publish.
time.sleep(10)
Controls publish frequency
10 seconds is a reasonable interval for environment sensors. Adjust based on how fast values change and broker rate limits.

## Slide 26
Publishing JSON Payloads
Structured data for dashboards and parsers
# Option A: Separate topics per measurement
client.publish("pico/temp", "24.5")
client.publish("pico/hum", "60.1")
# Option B: Single JSON topic (recommended)
import json
payload = json.dumps({
"temperature": temp,
"humidity": hum,
"pressure": pres,
"device": "pico2w_01"
})
client.publish("pico/sensors", payload)
# Example published JSON:
# {"temperature": 24.5, "humidity": 60.1,
# "pressure": 1013.2, "device": "pico2w_01"}
JSON vs Flat Topics
 | Flat Topics | JSON Payload
Topics | 3 publishes | 1 publish
Parsing | Simple | json.loads()
Node-RED | Multiple nodes | JSON node
Best for | Simple sensors | Multi-value
Home Assistant & Adafruit IO:
These platforms expect specific MQTT topic formats. Check their documentation for the exact topic structure and payload format.
Tip: Use json.loads(msg) on the subscriber side to parse incoming JSON. msg will be a bytes object — decode first: msg.decode()

## Slide 27
SECTION 07
Subscribing to MQTT Topics
Callbacks · set_callback() · wait_msg() · LED Control

## Slide 28
Subscribe — How It Works
Receiving messages from the broker
1
set_callback(fn)
Register a Python function that fires when a message arrives on any subscribed topic.
2
client.connect()
Connect to broker and establish persistent TCP session.
3
client.subscribe(topic)
Send SUBSCRIBE packet to broker. Broker notes this client wants topic messages.
4
wait_msg() / check_msg()
wait_msg() BLOCKS until a message arrives. check_msg() is non-blocking (returns None if no message).
5
Callback fires
When message arrives, broker sends PUBLISH → client calls your callback function with (topic, msg).
6
Act on message
Inside callback: decode msg, check content, control GPIO, update display, etc.

## Slide 29
Complete Subscribe Script — subscribe.py
Controlling Pico LED from MQTT messages
# subscribe.py — receive commands to control onboard LED
import time
from machine import Pin
from umqtt.simple import MQTTClient
from secrets import MQTT_SERVER, MQTT_PORT, MQTT_USER, MQTT_PASSWORD, MQTT_CLIENT_ID
# Hardware
led = Pin("LED", Pin.OUT) # onboard LED
# Topic to subscribe to
TOPIC_LED = "pico/led/control"
# Callback function — called when a message arrives
def callback(topic, msg):
print(f'Received: {topic} → {msg}')
if msg == b"ON" or msg == b"1":
led.on()
print("LED turned ON")
elif msg == b"OFF" or msg == b"0":
led.off()
print("LED turned OFF")
# Connect and subscribe
client = MQTTClient(MQTT_CLIENT_ID, MQTT_SERVER, MQTT_PORT,
MQTT_USER, MQTT_PASSWORD, ssl=True, ssl_params={"server_hostname": MQTT_SERVER})
client.set_callback(callback) # Register callback BEFORE connect
client.connect()
client.subscribe(TOPIC_LED)
print(f'Subscribed to {TOPIC_LED}')
# Main loop — wait for messages
while True:
client.wait_msg() # Blocks until a message arrives

## Slide 30
Subscribe Code — Deep Dive
Understanding every key line
set_callback(callback)
Must be called BEFORE connect(). The callback receives (topic: bytes, msg: bytes). Both are byte strings — compare with b"ON", not "ON".
msg == b"ON"
Messages arrive as bytes objects. Use b"..." literals or msg.decode() then compare strings. Never compare with plain strings directly.
client.subscribe(topic)
Registers interest with broker. Multiple calls allowed for different topics. One callback handles all — check topic inside callback.
wait_msg()
Blocks until ONE message arrives and calls callback. Use in a while True loop. For non-blocking: use check_msg() — returns None if no message.
check_msg()
Non-blocking alternative. Use when you have other tasks to run between checks. Call frequently (e.g., every 100ms) to avoid missing messages.
To subscribe to MULTIPLE topics: call client.subscribe() multiple times. Inside callback, check topic parameter to route messages correctly.

## Slide 31
Combined Publish + Subscribe Script
One Pico that both reads sensors AND receives commands
# main.py — publish sensor data AND subscribe to LED control
import time, json
from machine import Pin, I2C
import bme280
from umqtt.robust import MQTTClient
from secrets import *
led = Pin("LED", Pin.OUT)
i2c = I2C(0, sda=Pin(4), scl=Pin(5), freq=400000)
bme = bme280.BME280(i2c=i2c)
def on_message(topic, msg):
if topic == b"pico/led/control":
led.value(1 if msg == b"ON" else 0)
client = MQTTClient(MQTT_CLIENT_ID, MQTT_SERVER, MQTT_PORT,
MQTT_USER, MQTT_PASSWORD, ssl=True, ssl_params={"server_hostname": MQTT_SERVER})
client.set_callback(on_message)
client.connect()
client.subscribe("pico/led/control")
last_publish = 0
while True:
client.check_msg() # Non-blocking — check for incoming messages
if time.ticks_diff(time.ticks_ms(), last_publish) > 10000:
t = str(round(bme.temperature, 2))
client.publish("pico/bme280/temperature", t, retain=True)
last_publish = time.ticks_ms()
Key Design Pattern
Use check_msg() (non-blocking) instead of wait_msg() when publishing too. check_msg() returns immediately so you can run other tasks. Track publish timing with ticks_ms() difference — no blocking sleep() needed.

## Slide 32
umqtt.robust — Auto-Reconnect
Production-grade MQTT with reconnection handling
Problem with umqtt.simple
If the Wi-Fi or broker connection drops, simple.py raises an OSError exception and the script crashes. In a long-running IoT deployment, this is unacceptable.
# simple.py behavior on drop:
# OSError: [Errno 104] ECONNRESET
# Script halts — needs manual reset
# Bad for production deployments!
Symptoms:
• Pico stops publishing after broker restart
• No data on dashboard until manual Pico reset
• MQTT client disappears from broker list
Solution: umqtt.robust
robust.py extends simple.py with automatic reconnection. If the connection drops, it re-connects to the broker and re-subscribes automatically.
# Just change the import!
# FROM:
from umqtt.simple import MQTTClient
# TO:
from umqtt.robust import MQTTClient
Benefits:
• Reconnects automatically on Wi-Fi drop
• Re-subscribes to all topics after reconnect
• No script changes beyond the import line
→ Always use umqtt.robust for production and long-running deployments. Use umqtt.simple only for learning and quick experiments.

## Slide 33
SECTION 08
Testing & Troubleshooting
MQTT Explorer · HiveMQ WebUI · Debug Tips · Common Errors

## Slide 34
Testing with MQTT Explorer
Visual tool to monitor topics and publish test messages
1
Download
Get MQTT Explorer free from: mqtt-explorer.com. Available for Windows, macOS, Linux.
2
Connect
Enter broker URL, port 8883, username, password, enable TLS. Click Connect.
3
Monitor Topics
All topics published by your Pico 2W appear in the left panel as a tree. Click any topic to see its current value and history.
4
Publish Test
Right side: enter topic (e.g. pico/led/control), type payload (ON or OFF), click Publish. Your Pico receives it instantly.
5
Verify
Check Thonny Shell on Pico side — the callback print() should show the received message confirming end-to-end success.
Other Test Tools
HiveMQ Web Client
Built-in browser client at hivemq.com/demos/websocket-client/
MQTT.fx
Desktop client, good for scripted testing
mosquitto_pub / _sub
CLI tools — fast for command-line testing
Node-RED
Flow-based dashboard with MQTT nodes
Home Assistant
Full HA integration with MQTT Discovery

## Slide 35
Troubleshooting Common Issues
Symptoms, causes, and fixes
Symptom | Likely Cause | Solution
OSError: ECONNRESET | MQTT connection dropped (Wi-Fi or broker restarted) | Switch to umqtt.robust for auto-reconnect
MQTTException: 5 | Wrong username or password for broker | Double-check credentials in secrets.py
OSError: -2 | Hostname not resolved (DNS failure or wrong URL) | Verify cluster URL, check Wi-Fi is connected first
Script hangs on connect() | Port mismatch: using 1883 on TLS-only broker | Use port 8883 with ssl=True for HiveMQ
Callback never fires | set_callback() called after connect() | Always call set_callback() BEFORE connect()
msg comparison fails | Comparing msg == 'ON' instead of b'ON' | Messages are bytes — use b'ON' or msg.decode()
Only publishes once | wait_msg() inside publish loop blocks indefinitely | Use check_msg() for non-blocking message checks
Broker disconnects Pico | Duplicate Client ID on same broker | Use unique MQTT_CLIENT_ID per physical device

## Slide 36
Debugging Tips & Best Practices
Making MQTT development easier
Print broker responses
Add try/except around connect() and print the exception. MQTTException code 5 = bad credentials; 128+ = protocol error.
Test topics in isolation
Use MQTT Explorer to publish to pico/led/control manually BEFORE running subscribe script. Isolates server vs client issues.
Check Thonny Shell
All print() output from Pico appears in Thonny Shell. Add verbose prints in callback to trace every received message.
Verify Wi-Fi before MQTT
Print wlan.isconnected() and wlan.ifconfig() before attempting MQTT connect. No Wi-Fi = connection will always fail.
Use retained messages
Publish with retain=True so MQTT Explorer shows the LAST value immediately when you connect — great for debugging state.
Binary vs string compare
Print type(msg) inside callback. It will show <class 'bytes'>. Use msg.decode() == 'ON' or msg == b'ON'.

## Slide 37
MQTT with Node-RED Dashboard
Visualizing Pico sensor data in real time
Node-RED MQTT Setup
1
Install Node-RED
npm install -g node-red (on Raspberry Pi or PC)
2
Open browser
Navigate to http://localhost:1880
3
Add MQTT-in node
Drag 'mqtt in' node. Configure broker URL, port, credentials.
4
Set topic
Set topic to pico/bme280/# (wildcard for all sensor readings)
5
Add dashboard
Install node-red-dashboard, add 'gauge' or 'chart' nodes
6
Connect & Deploy
Wire MQTT-in → JSON → Gauge. Click Deploy. Open /ui dashboard.
Node-RED Flow
mqtt in
pico/bme280/#
json
Parse JSON
gauge
Temperature
chart
History
Other MQTT Platforms:
Home Assistant · Adafruit IO · OpenHAB · Grafana + InfluxDB

## Slide 38
Home Assistant MQTT Integration
Connecting Pico 2W to home automation
# MQTT Discovery for Home Assistant
# HA auto-detects device if you publish to correct topic
import json
# Step 1: Publish device discovery config
config_topic = "homeassistant/sensor/pico_temp/config"
config_payload = json.dumps({
"name": "Pico Temperature",
"device_class": "temperature",
"state_topic": "pico/bme280/temperature",
"unit_of_measurement": "°C",
"unique_id": "pico2w_temp_01"
})
client.publish(config_topic, config_payload, retain=True)
# Step 2: Publish sensor data as usual
# home/pico/bme280/temperature → HA reads it automatically
client.publish("pico/bme280/temperature", str(temp), retain=True)
HA MQTT Discovery
Enable MQTT integration in HA Settings → Devices
Configure broker URL (same HiveMQ or local Mosquitto)
Publish config payload to homeassistant/<domain>/<id>/config
HA auto-creates entity — appears in dashboard immediately
State updates flow via state_topic — same as regular publish
MQTT Discovery eliminates manual HA entity config. Publish the config JSON once and HA auto-discovers your Pico as a device with all its sensors.

## Slide 39
Advanced: Last Will & Testament (LWT)
Knowing when your Pico goes offline
What is LWT?
LWT lets you specify a message that the broker publishes AUTOMATICALLY if your Pico disconnects ungracefully (power loss, Wi-Fi drop, crash). Other subscribers receive the offline notice immediately.
# Set LWT before calling connect()
client.set_last_will(
topic = "pico/status",
msg = "offline",
retain = True,
qos = 1
)
client.connect() # LWT registered in CONNECT packet
When Pico connects cleanly, it publishes 'online' itself. The broker sends 'offline' only on ungraceful disconnect.
LWT Use Cases
Device presence
Dashboard shows 🟢 online / 🔴 offline per device
Alert system
Node-RED sends email if device goes offline unexpectedly
HA availability
Home Assistant uses LWT to mark entity as unavailable
Fleet monitoring
Track which of many Pico devices are currently active
# On clean boot: announce online status
client.publish("pico/status", "online", retain=True)

## Slide 40
Summary & Key Takeaways
What you've learned in this lecture
MQTT Protocol
Lightweight pub/sub over TCP. RFC 6455. Ports 1883 (plain) / 8883 (TLS). Minimal overhead — perfect for IoT.
Core Concepts
Publish, Subscribe, Topics (hierarchical, case-sensitive), Messages (any payload), Broker (filters & routes).
Broker Setup
HiveMQ free cloud (no install), Mosquitto local (Raspberry Pi), or cloud VPS. Need URL, port, username, password.
umqtt Modules
simple.py = basic MQTT client. robust.py = auto-reconnect. Install in /umqtt/ folder on Pico filesystem.
secrets.py
Store all credentials in secrets.py. Never hardcode in main script. Add to .gitignore.
Publishing
MQTTClient → connect() → publish(topic, msg, retain=True). Use JSON for multi-value payloads.
Subscribing
set_callback() BEFORE connect(). subscribe(topic). wait_msg() blocks; check_msg() non-blocking.
Production Tips
Use robust.py, unique client IDs, LWT for offline detection, check_msg() for multi-task loops.

## Slide 41
MicroPython MQTT — Quick Reference Cheat Sheet
Raspberry Pi Pico 2W · umqtt.simple / umqtt.robust
# Connect to broker
from umqtt.robust import MQTTClient
client = MQTTClient(client_id, server,
port, user, pwd, ssl=True,
ssl_params={"server_hostname": server})
client.set_callback(callback_fn)
client.connect()
# Publish
client.publish(topic, msg)
client.publish(topic, msg, retain=True)
# Subscribe
client.subscribe("home/+/lamp")
# Wait: blocking / non-blocking
client.wait_msg()
client.check_msg()
# Callback template
def callback(topic, msg):
t = topic.decode()
m = msg.decode()
if t == "pico/led":
led.value(1 if m=="ON" else 0)
# Pub + Sub main loop
last = 0
while True:
client.check_msg() # non-blocking
if time.ticks_diff(time.ticks_ms(), last) > 10000:
client.publish(topic, data, retain=True)
last = time.ticks_ms()
# LWT: client.set_last_will(topic, 'offline', retain=True, qos=1) — BEFORE connect()

## Slide 42
Review Questions & Lab Checklist
Verify your understanding
Review Questions
What does MQTT stand for, and what is its primary design goal?
Explain the publish/subscribe model. How does it differ from HTTP?
What is the role of the MQTT broker? Name two broker options.
What are MQTT topic wildcards? Give an example of + and # usage.
What is the difference between QoS 0, 1, and 2?
Why must set_callback() be called BEFORE connect()?
What is the difference between wait_msg() and check_msg()?
Why use umqtt.robust instead of umqtt.simple in production?
What happens if two devices share the same MQTT Client ID?
How do MQTT retained messages benefit late-joining subscribers?
Lab Checklist
HiveMQ account created & cluster URL saved
umqtt/simple.py uploaded to Pico
umqtt/robust.py uploaded to Pico
secrets.py created with correct credentials
boot.py connects Pico 2W to Wi-Fi
publish.py sends BME280 data successfully
subscribe.py controls Pico LED from MQTT
MQTT Explorer shows published topics
Multi-client test: two subscribers update together
Bonus: Node-RED or HA dashboard running

## Slide 43
End of Lecture
Raspberry Pi Pico 2W — Getting Started with MQTT
MicroPython · umqtt · HiveMQ · Pub/Sub · BME280 · Node-RED
You can now connect any Pico 2W sensor to any MQTT-enabled platform!